## Slide 1: RMCAT Application Interaction
draft-ietf-rmcat-app-interaction-01
Mo Zanaty, Varun Singh,
Suhas Nandakumar, Zahed Sarker
IETF 91

## Slide 2: Goals
Agree on the conceptual decomposition of RMCAT applications to describe interfaces and interactions between congestion control and other functions
Agree on the critical interfaces and interactions
Decide if only informative for normalizing evaluations of solution candidates, or should contain normative language for the scope and interfaces of congestion controllers

## Slide 3: Changes since -00
Focus on top 5 interfaces and interactions
  Section 5 now has an overview of the top 5 interactions
      Allowed Rate (CC-Codec)
      Startup Ramp (CC-Codec)
      Delay Tolerance (CC-Codec)
      Loss Tolerance (CC-Codec)
      Priority / Weight (Config-CC-UDP)
    Solution candidates: Please review and provide feedback if these are the top interactions for your algorithm!
  Sections 5.x provide further details and more interactions
Replace OS with Network Stack
  Acknowledge that user-space stacks are also possible

## Slide 4: Conceptual Model
Network
Stack
Application
UDP
Config
Codec
Congestion Control
RTP
Shared State
Shared State
RTCP
socket interface and other network functions, e.g. ECN, DSCP, PHY events, shaping
media and transport configuration, e.g. SDP, WebRTC API constraints,
RTP/RTCP, CC

## Slide 5: Conceptual Model - Top 5 Interactions
Network
Stack
Application
UDP
Config
Codec
Congestion Control
RTP
Shared State
Shared State
RTCP
socket interface and other network functions, e.g. ECN, DSCP, PHY events, shaping
Allowed Rate
Startup Ramp
Delay Tolerance
Loss Tolerance
Priority

## Slide 6: Open Questions
Should the top interactions include Media Elasticity?
(range, granularity and convergence time of rate changes)
Informative-only or normative language for the scope and interfaces/interactions of congestion controllers?
Are we providing the right guidance to congestion control designers and application developers?
Are we facilitating evaluation and comparison of solution candidates by normalizing the interfaces and interactions?
Should we move RTP Circuit Breakers (non-) interaction to requirements?